## Slide 1: Unit 1: An Overview of Electrical Machines Use and Maintenance

## Slide 2: Unit-1
Outlines:
Application of electrical machines in industries and utilities such as processing industry, power plants, transports, etc.
Consequences of equipment failures;
Techniques to avoid failure of machines;
Breakdown versus condition-based-maintenance.

## Slide 3: As learners, we must put more of an emphasis on LISTENING than on working alone!
Introductions: Overview of Electrical Machine
Electrical machine are devices that convert electrical energy into mechanical energy or vice versa.
The main type of electrical machine are:
Generators (convert mechanical energy into electrical energy)
Motors (convert electrical energy into mechanical energy)
Transformers (Transfer electrical energy between two or more circuit through electromagnetic induction)

## Slide 4: As learners, we must put more of an emphasis on LISTENING than on working alone!
Application of electrical machines in industries and utilities such as processing industry, power plants, transports, etc.
Application of electrical machines in:
1. Industrial Applications
Electrical machines are integral to manufacturing industries, driving various types of machinery and equipment essential for production.
Their applications range from powering basic tools, conveyers systems to enabling the advance automation and robotics:
Here’s the few example of applications of electrical machines particularly in the manufacturing industries.

## Slide 5: As learners, we must put more of an emphasis on LISTENING than on working alone!
Machine tools
Induction motors and Servo motors:
  Lathes: Used for turning operations where raw material is shaped into a cylindrical form.
  Milling Machines: Used for cutting and shaping metal or other materials.
  Grinders: Used for finishing operations to achieve high surface quality and precision.
  Drilling Machines: Used for making holes in various materials.
2. Conveyor Systems
Induction Motors:
  a) Material Handling: Motors drive conveyor belts for transporting materials and products through different stages of manufacturing.

## Slide 6: As learners, we must put more of an emphasis on LISTENING than on working alone!
3. Robotics and Automation
Servo Motors and Stepper Motors:
  a) Robotic Arms: These motors provide precise control and positioning for tasks such as welding, painting, assembly, and packaging.
  b) Automated Guided Vehicles (AGVs): Motors drive AGVs used for transporting materials within the factory.
4. Pumps and Compressors
Induction Motors:
  a) Hydraulic Systems: Motors drive hydraulic pumps used in presses, injection molding machines, and other equipment requiring hydraulic power.
  b) Air Compressors: Used to power pneumatic tools and equipment, as well as for general plant air supply.

## Slide 7: As learners, we must put more of an emphasis on LISTENING than on working alone!
5. Mixers and Agitators
Induction Motors:
  Mixing Equipment: Motors drive mixers and agitators used in processes such as blending, emulsifying, and homogenizing materials.
6. Fans and Blowers
Induction Motors:
  a) Ventilation and Cooling: Motors drive fans and blowers for ventilation, cooling, and air circulation in manufacturing plants.

## Slide 8: As learners, we must put more of an emphasis on LISTENING than on working alone!
7. Packaging Machinery
Induction Motors and Servo Motors:
  a) Filling Machines: Motors drive filling machines for liquids, powders, and granules.
  b) Sealing and Labeling: Motors power machines for sealing packages and applying labels.
8. Welding Equipment
Induction Motors:
  a) Spot Welders and Seam Welders: Motors are used in welding equipment for joining metal parts, which is essential in automotive and metal fabrication industries.
9. CNC Machines
Servo Motors:
  a) Computer Numerical Control (CNC): Servo motors provide precise control for CNC machines used in cutting, drilling, and milling operations.

## Slide 9: As learners, we must put more of an emphasis on LISTENING than on working alone!
10. Electric Generators
Standby and Backup Power:
  a) Continuous Operations: Generators provide backup power to ensure uninterrupted operations during power outages.

## Slide 10: As learners, we must put more of an emphasis on LISTENING than on working alone!
2. Processing Industrial
Motors:
  a) Pumps and Compressors: Induction motors and synchronous motors are widely used to drive pumps and compressors in chemical, petrochemical, and water treatment plants.
  b) Conveyors and Material Handling: Motors power conveyor belts, hoists, cranes, and automated material handling systems.
  c) Mixers and Agitators: Electrical motors drive mixers, agitators, and other equipment used in food processing, pharmaceuticals, and chemical industries.

## Slide 11: As learners, we must put more of an emphasis on LISTENING than on working alone!
2. Generators:
  Backup Power:
  Generators provide backup power for critical processes and machinery in case of power outages.
  b) Co-generation:
  Combined heat and power (CHP) systems use generators to produce both electricity and useful thermal energy from a single fuel source.

## Slide 12: As learners, we must put more of an emphasis on LISTENING than on working alone!
3. Power Plants
Generators:
  a) Electricity Generation: Synchronous generators are used in thermal, hydroelectric, nuclear, and renewable energy power plants to generate electricity.
  b) Excitation Systems: DC machines are used in the excitation systems of large synchronous generators to control the output voltage.
Motors:
  a) Auxiliary Systems: Induction motors are used in auxiliary systems such as feedwater pumps, cooling water pumps, and fans in power plants.
  b) Control Systems: Stepper motors and servo motors are used in various control systems for precise positioning and control tasks.

## Slide 13: As learners, we must put more of an emphasis on LISTENING than on working alone!
4. Transport
Electric Vehicles (EVs):
  a) Traction Motors: Induction motors and permanent magnet synchronous motors (PMSMs) are used in electric and hybrid vehicles for propulsion.
  b) Regenerative Braking: Electric machines enable regenerative braking, which recovers kinetic energy during braking and converts it back to electrical energy.
Railway Systems:
  a) Locomotives: Synchronous motors and induction motors are used in electric and diesel-electric locomotives.
  b) Light Rail and Metros: Electric motors power light rail vehicles, metro trains, and trams for urban transportation.

## Slide 14: As learners, we must put more of an emphasis on LISTENING than on working alone!
5. HVAC Systems:
a) Fans and Blowers: Motors drive fans and blowers in heating, ventilation, and air conditioning (HVAC) systems.
b) Compressors: Motors power compressors in refrigeration and air conditioning systems.
6. Renewable Energy:
a) Wind Turbines: Synchronous generators and induction generators are used in wind turbines to convert wind energy into electrical energy.
b) Hydroelectric Plants: Synchronous generators are used in hydroelectric plants to generate electricity from water flow.

## Slide 15: As learners, we must put more of an emphasis on LISTENING than on working alone!
2. Consequences of Equipment Failures.
There are several serious consequence of the electrical equipment failures, here are few examples of cause of electrical equipment failures in generals:
Repair and Replacement Costs:
The immediate cost of repairing or replacing failed equipment can be substantial.
2. Loss of Revenue:
Downtime and reduced productivity can result in lost revenue.
3. Loss of Productivity:
Unplanned outages and the time required for repairs can result in lost productivity.
4. Brand Damage:
Repeated failures can harm a company's reputation and brand value.

## Slide 16: As learners, we must put more of an emphasis on LISTENING than on working alone!
5. Impact on Other Systems:
Failures in one piece of equipment can cascade, affecting other connected systems and equipment.
6. Electrical Fires:
Faulty equipment can cause sparks or overheat, leading to fires.
7. Explosions:
Certain electrical failures can lead to explosions, particularly in environments with flammable materials.
8. Employee Morale:
Frequent failures and the associated stress can lower employee morale and job satisfaction.

## Slide 17: As learners, we must put more of an emphasis on LISTENING than on working alone!
3. Techniques to Avoid Failure of Machines
Think pair share (5 minutes)
What causes the electrical equipment to fail?
What are some of the remedial actions to avoid the equipment failures?
Can you name some of the techniques used to diagnose the electrical faults in electrical machines?

## Slide 18: As learners, we must put more of an emphasis on LISTENING than on working alone!
What causes the electrical equipment to fail?
The main reasons, for equipment failure are related to poor manufacturing quality, like defective casting or jointing.
Another common reason is the improper use of the machines. For example, overcurrent due to jam conditions of the rotor may pose a threat to the health of the machines.
The main causes that lead to failures in electrical machines is presented:
Harsh environment;
Improper machine selection and application;
Inadequate installation;
Mechanical failure;
Electrical problems;
Voltage unbalance;
Inadequate maintenance;
Combination of one or more of the abovementioned causes.

## Slide 19: As learners, we must put more of an emphasis on LISTENING than on working alone!
What causes the electrical equipment to fail?
One of the most common reasons for fault propagation is a harsh environment.
One of the elements of the harsh environment is the excessive temperature due to environmental reasons or problems in the motor.
To ensure a long-lasting exploitation time of the machines, they must operate on the nominal temperature rating.
Every 10°C of overheating means halving of insulation life time and can lead to different insulation problems.

## Slide 20: As learners, we must put more of an emphasis on LISTENING than on working alone!
What causes the electrical equipment to fail?
Another common environmental factor that can cause machine failures is moisture. If for any reasons moisture forms on the surface of the machine insulation, the insulation may become conductive and result in insulation and whole machine failure.
There is also a possibility that the insulation would absorb the moisture from its surface in time, which will cause the insulation resistance to lower to the level that a fault will occur.
Apart from the mentioned ones, there are numerous harmful environments – the ones containing harmful gases and fumes, salt rich air, excessive dirt, dust, etc.

## Slide 21: As learners, we must put more of an emphasis on LISTENING than on working alone!
What causes the electrical equipment to fail?
Machines are usually coupled with some sort of load.
This means that all those couplings, belts and other connections between the machine and the load must be aligned correctly, otherwise excessive vibrations might occur, which can be potentially damaging for the machine.
Excessive vibrations can also occur due to wrongly sized or not enough tightened mounting bolts.
Those vibrations can be extremely harmful to bearings and shaft of the machine and can even cause winding burnout.

## Slide 22: As learners, we must put more of an emphasis on LISTENING than on working alone!
What causes the electrical equipment to fail?
One of the common causes of machine failure is overloading of the machines.
If for some reason excessive load is connected to the motor, the motor will draw additional current and as a result the machine temperature will increase.
Due to exceeding of the rated full load current and most probably nominal temperature ratings, the machine exploitation time will be shortened.
In some occasions, jam conditions of the rotor can be the source for overloading of the machine.
This in turn can often be caused by a bearing failure that is considered to be one of the most common machine faults.

## Slide 23: As learners, we must put more of an emphasis on LISTENING than on working alone!
What causes the electrical equipment to fail?
If the supply voltage of the electrical machine has been chosen incorrectly, it can shorten the life period of the machine.
In some cases, when the voltage deviations become severe, it can result in rapid failure of the machine.
Copper losses can be reduced with high line voltage, but on the other hand, increased magnetic flux will result in higher iron losses.
Tests have shown that if the supply voltage rises in the order of 10% or more over the rated voltage, it will cause the iron to saturate and will lead to harmful overheating of the machine.

## Slide 24: As learners, we must put more of an emphasis on LISTENING than on working alone!
What causes the electrical equipment to fail?
Unbalanced voltage between the phases can also be harmful for the machines, as they will lead to current unbalance, which will again result in overheating of the machine.
This problem is becoming more and more severe due to excessive harmonics in the grid and the addition of nonlinear loads in the end user side of the grid.
Those harmonics and unexpected nonlinear loads may also lead to unbalanced current of the machine and become harmful not only to the machine itself, but also to power electronic converters, which are very often used in hand with electrical machines.

## Slide 25: As learners, we must put more of an emphasis on LISTENING than on working alone!
What are some of the remedial actions to avoid the equipment failures?
Traditional types of maintenance can be generally classified into two categories:
Corrective and
Preventive maintenance.
In the case of corrective maintenance, also known as Reactive maintenance, all needed control and repairs are assumed to the equipment after the failure has already occurred.
On other hand, it is possible to assume preventive maintenance to the electrical equipment in order to avoid catastrophic outcomes.
In this case, the electrical equipment needs to be regularly checked through scheduled and specified inspections.

## Slide 26: As learners, we must put more of an emphasis on LISTENING than on working alone!
What are some of the remedial actions to avoid the equipment failures?
Other ways to avoid failure are according to the number and position of sensors, the diagnostic techniques can be divided into two main catégories:
Non-invasive techniques and
Invasive techniques.
The techniques where there is no built-in sensor in the equipment to get any measurements are called non-invasive techniques.
These techniques are cheap and flexible in the way that the signals of interest can be measured anywhere away from the actual physical system.
But these techniques are less accurate because of the external environmental factors.
The motor current measurement using clamp meters is a very common example of non-invasive techniques.

## Slide 27: As learners, we must put more of an emphasis on LISTENING than on working alone!
What are some of the remedial actions to avoid the equipment failures?
In invasive techniques, sensors are embedded in the equipment.
For example, the thermistors or positive temperature coefficient (PTC) sensors can be placed inside the coils of the transformer or motor for the measurement of temperature.
These techniques are more accurate but costly as well.

## Slide 28: As learners, we must put more of an emphasis on LISTENING than on working alone!
What are some of the remedial actions to avoid the equipment failures?
However the recent development of Diagnostics and condition monitoring is one of the key factors that can prevent or at least delay the occurring failure.
From here on and in the preceding units we will completely focus our energy in understanding the Condition Monitoring of Electrical Machine.
Most faults start as minor deviations from the normal conditions and they seem unimportant.
The problem is that if those small deviations are not dealt with in time, the faults can start propagating until the repair of the machine is not reasonable or even possible.
When condition monitoring or online diagnostic measures are taken, it is possible to detect the faults at early stages and save the machine from larger faults in time.

## Slide 29: As learners, we must put more of an emphasis on LISTENING than on working alone!
What is mean by Condition Monitoring of electrical machine?
The algorithms train models based on the data collected from electrical machines and drives, which help us detect faults in their initial stages.
This helps to reduce the damage and also to identify the faults, which need immediate attention.
This is generally known as condition monitoring of electrical machine.
Figure1: General Overview of Condition monitoring

## Slide 30: As learners, we must put more of an emphasis on LISTENING than on working alone!
3. Can you name some of the techniques used to diagnose the electrical faults in electrical machines?
In a broader domain, the diagnostic techniques can be divided into the following categories:
Electromagnetic field monitoring, search coils, coils wound around motor shafts (axial flux related detection)
Temperature measurements
Infrared recognition
Radio-frequency (RF) emissions monitoring
Noise and vibration monitoring
Chemical analysis
Acoustic noise measurements
Motor-current signature analysis (MCSA)
Model, artificial intelligence, and neural-network-based techniques.

## Slide 31: As learners, we must put more of an emphasis on LISTENING than on working alone!
4.Breakdown Versus Condition-based-maintenance.
Breakdown Maintenance (Reactive Maintenance)
1. Unplanned:
Maintenance activities are not scheduled; they occur in response to equipment failure.
2. Immediate Action Required:
Repairs need to be carried out immediately to minimize downtime.
3. Higher Downtime:
Equipment downtime is typically longer because repairs are unplanned and may require time to diagnose and fix the issue.

## Slide 32: As learners, we must put more of an emphasis on LISTENING than on working alone!
4.Breakdown Versus Condition-based-maintenance.
4. Higher Cost:
Often leads to higher costs due to emergency repairs, overtime labor, and potential secondary damage to equipment.
5. Limited Life Cycle Management:
Focus is on immediate fixes rather than extending the overall life of the equipment.

## Slide 33: As learners, we must put more of an emphasis on LISTENING than on working alone!
4.Breakdown Versus Condition-based-maintenance.
2. Condition-Based Maintenance (CBM) (Predictive Maintenance)
Planned and Predictive:
Maintenance is scheduled based on the actual condition and performance data of the equipment.
2. Monitoring and Analysis:
Utilizes sensors, diagnostics, and data analysis tools to monitor equipment health.
3. Reduced Downtime:
Maintenance can be planned and performed before a failure occurs, reducing unplanned downtime.

## Slide 34: As learners, we must put more of an emphasis on LISTENING than on working alone!
4.Breakdown Versus Condition-based-maintenance.
2. Condition-Based Maintenance (CBM) (Predictive Maintenance) cont…..
4. Optimized Maintenance Intervals:
Maintenance activities are performed only when necessary, extending equipment life and reducing unnecessary maintenance.
5. Higher Initial Investment:
Requires investment in monitoring systems and technology.

## Slide 35: As learners, we must put more of an emphasis on LISTENING than on working alone!
Merits and Demerits of Breakdown Versus Condition-based-maintenance
 | Break Down | Condition based
Advantages | Simplicity | Improved Reliability
 | Short-term cost saving | Better Resource Allocation
Disadvantages | Unpredictability | Higher Initial Costs
 | Higher Long-Term Costs | Complexity

## Slide 36: As learners, we must put more of an emphasis on LISTENING than on working alone!
References: