## Slide 1: Unit 2: Introduction to Condition Monitoring

## Slide 2: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively.
Outlines:
Condition monitoring overview and purpose;
Common condition monitoring techniques;
Invasive and non-invasive methods; Sensors, data acquisition, and overview of signal pre-processing for condition monitoring.

## Slide 3: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Introductions: Overview of Conditioning Monitoring
The speed of rotating machinery, together with the capabilities of their control and processing systems, are now improving at an ever-increasing rate.
Many of these machines are currently being designed to operate almost super critically, and this trend is likely to continue under the competitive demands of the marketplace.
Thus, the monitoring and control of excessive vibration, noise, thermal variation, dust and dangerous emissions from plant and machinery of various types are now required by law in many countries.
In addition, a large number of countries are also applying strict liability legislation in respect of defective products.
This has been done under various Acts and Directives, which have been formulated to protect a nation's society from the dishonest application of technology.
Accordingly, anyone who suffers harm as a result of a defective product or process can now recover compensation from those liable for the injury.

## Slide 4: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Introductions: Overview of Conditioning Monitoring
Therefore, properly used, condition monitoring can identify most, if not all, of the factors limiting the effectiveness and efficiency of the total plant.
Poor design standards, purchasing practices, improper operation and outdated management methods, contribute more to high production and maintenance costs than do delays caused by the catastrophic failure of critical plant machinery.
As a maintenance management tool, condition monitoring can provide the data required to schedule both preventive and corrective maintenance tasks on an as-needed basis instead of relying on industrial average life statistics, such as Mean Time To Failure (MTTF), to schedule maintenance activities.
Condition monitoring uses direct monitoring of the operating condition, system efficiency and other indicators to determine the actual MTTF or loss of efficiency for each machine train and system within the plant.

## Slide 5: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Introductions: Overview of Conditioning Monitoring
The addition of a comprehensive condition monitoring programme, can and will, provide factual data defining the actual mechanical condition of each machine train and operating efficiency of each process system.
This data provides the maintenance manager with factual information that can then be used to schedule maintenance activities.
A condition monitoring programme can minimize unscheduled breakdowns of all mechanical equipment in the plant, and ensure that repaired equipment is in an acceptable mechanical condition.
The programme can also identify machine train problems before they become serious.
Most problems can be minimized if they are detected and repaired early.

## Slide 6: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Introductions: Overview of Conditioning Monitoring
Condition monitoring can also be an invaluable production management tool.
The data derived from a comprehensive programme can provide the information needed to increase production capacity, product quality and the overall effectiveness of the production function.
Condition monitoring can provide the data needed to achieve optimum and consistent reliability, capacity and efficiency from critical production systems.
While these parameters are viewed as maintenance responsibilities, many of the factors directly affecting them are outside the maintenance function.
Product quality and total production costs are other areas where condition monitoring can benefit production management.

## Slide 7: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Introductions: Overview of Conditioning Monitoring
Figure 1: Schematic of History of evaluation Industrial Evaluations
What is relation between history of evaluation of industry and conditioning monitoring?
As we can see from figure 1, industry 4.0 is packed with smart sensors, IoT, Cyber-Physical Systems and Cloud and Networks.
So, it is the era of AI.
When more sophisticated integrations are introduced, Condition Monitoring becomes necessary to keep a certain electric power quality and supply reliability level in the new dispersed and dynamic systems.

## Slide 8: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Introductions: Overview of Conditioning Monitoring
Figure 2: Electrical machines fault statistics according to IEEE survey
According to fault statistics by IEEE survey presented in figure 2, electrical machines are prone to failure.
Early detection of faults in mentioned parts of the electrical equipment as shown in figure 2, can be possible with Condition Monitoring.
Early detection of fault and timely maintenance of machineries can prolong the life of equipment, reduce the maintenance and repair cost and over all, improve the efficiency of the plant.

## Slide 9: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Figure 3: Electrical machines fault statistics according to IEEE, EPRI and Allianz survey

## Slide 10: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Introductions: Overview of Conditioning Monitoring
In 2015, ABB predicted that there were approximately 300 million asynchronous motors in use worldwide, with an estimated annual growth rate of 10%.
By 2020, it was estimated that around 480 million asynchronous motors would be in use.
Statistically, various premature failures occur in about 5 to 6 % of electric motors, equivalent to around 20 to 25 million motors.
According to statistics, issues related to stator currents in asynchronous motors controlled by frequency converters may affect roughly 0.25% of electric machines, or approximately one million motors.

## Slide 11: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Introductions: Overview of Conditioning Monitoring
Fault diagnostics and condition monitoring of electrical machines have always been one of the primary concerns in the industry.
With the advent of industry standards 4.0, condition monitoring and predictive maintenance have become the forefront of current research areas.
Electrical machines play a significant role in multiple domestic and industrial applications, so keeping track of their health is essential.
Due to the environment, constant running, external and internal stresses and other parameters constantly affecting electrical machines, there is a high chance of fault occurrence.

## Slide 12: As learners, we must put more of an emphasis on LISTENING than on working alone!
What is mean by Condition Monitoring of electrical machine at nut cell?
The algorithms train models based on the data collected from electrical machines and drives, which help us detect faults in their initial stages.
This helps to reduce the damage and also to identify the faults, which need immediate attention.
This is generally known as condition monitoring of electrical machine.
Figure4: General Overview of Condition monitoring

## Slide 13: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
What is the main PURPOSE of Condition monitoring?
1. Early Detection of Faults:
Identifying potential issues before they lead to equipment failure.
This helps in planning maintenance activities proactively rather than reactively.
2. Preventive Maintenance:
Scheduling maintenance based on the actual condition of equipment rather than fixed intervals.
This approach can extend the life of the equipment and reduce unnecessary maintenance tasks.
3. Improved Reliability:
Enhancing the reliability and availability of machinery and systems by ensuring they are always in optimal working condition.

## Slide 14: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
What is the main PURPOSE of Condition monitoring?
4. Cost Savings:
Reducing maintenance costs by preventing major failures and optimizing maintenance schedules.
Avoiding unexpected downtime can also lead to significant cost savings.
5. Safety:
Ensuring the safe operation of machinery by detecting issues that could lead to hazardous situations.
This is particularly important in industries where equipment failure can have severe safety implications.

## Slide 15: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
2. Common Condition Monitoring Techniques;
The common condition monitoring techniques which are recently becoming the topic of interest and aligned with the Industry 4.0 standards are:
Table below shows the recent condition monitoring techniques.
In the table ref. column shows the reference paper numbers, whose references are given in the reference section at the end of slides.

## Slide 17
Table 2: Comparison of the Main Algorithms For Condition Monitoring.

## Slide 18
Table 2: Comparison of the Main Algorithms For Condition Monitoring.

## Slide 19
Table 2: Comparison of the Main Algorithms For Condition Monitoring.

## Slide 20: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
3. Invasive and Non-invasive Methods; Sensors, Data Acquisition, and Overview of Signal Pre-processing for Condition Monitoring.
Diagnostic of electrical machines has been an investigative interest for researchers for the past few decades.
This also means that there are several diagnostic methods available that are used to identify the faults in machines.
According to the number and position of sensors, the diagnostic techniques can be divided into two main catégories – non-invasive techniques and invasive techniques.

## Slide 21: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
1. Non-invasive Techniques
The techniques where there is no built-in sensor in the equipment to get any measurements are called non-invasive techniques.
These techniques are cheap and flexible in the way that the signals of interest can be measured anywhere away from the actual physical system.
But these techniques are less accurate because of the external environmental factors.
The motor current measurement using clamp meters is a very common example of non-invasive techniques.
The other examples are torque and speed measurements and thermal cameras etc.

## Slide 22: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
2. Invasive Techniques
In invasive techniques, sensors are embedded in the equipment.
For example, the thermistors or positive temperature coefficient (PTC) sensors can be placed inside the coils of the transformer or motor for the measurement of temperature.
These techniques are more accurate but costly as well.
In a broader domain, the diagnostic techniques can be divided into the following categories:
1) Electromagnetic field monitoring, search coils, coils wound around motor shafts (axial flux related detection)
2) Temperature measurements
3) Infrared recognition

## Slide 23: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
4) Radio-frequency (RF) emissions monitoring
5) Noise and vibration monitoring
6) Chemical analysis
7) Acoustic noise measurements
8) Motor-current signature analysis (MCSA)
9) Model, artificial intelligence, and neural-network-based techniques.
However, almost all of the above-mentioned techniques depend upon the tools depicted in the following Fig. 5.

## Slide 24: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Figure 5: Classification of fault diagnostic techniques

## Slide 25: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Key Components of Condition Monitoring:
Sensors:
Devices used to measure various physical parameters such as vibration, temperature, pressure, and more.
2. Data Acquisition:
The process of collecting data from sensors and converting it into a digital format for analysis.
3. Signal Pre-processing:
Techniques used to filter, transform, and prepare raw sensor data for further analysis.

## Slide 26: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Figure 6: Overview of Sensors, data acquisition and Signal Pre-processing in condition monitoring

## Slide 27: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Sensing Elements:
Use temperature sensors to sense the thermal condition of inter parts of machine.
Use tachometer to read the speed of the rotor.
Use ammeter and clamp meter to read magnitude of current signals
Use voltmeter to read voltage magnitude supplied.
Use Infrared Sensors to measure gas concentration based on the absorption of infrared light by gas molecules.
Piezoelectric Sensors to detect high-frequency sound waves generated by cracks or other structural changes in materials.
Transducer convert mechanical signals into electrical signals.

## Slide 28: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Data Acquisition and signal conditioning :
Collect signals and data from various sensors and convert it into digital/analog signals as per the requirement.
It will add feedbacks, magnify/amplify the signals, chop, filter the signals and conditions the signals.
Eliminations and manipulation of signals are done here.
Over all modification of signals received from the sensing elements and readying for the signal processing.

## Slide 29: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Figure 7: Generalized block diagram for data acquisition

## Slide 30: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Signal Processing Elements/Units :
Analyze the input signal and perform the operation on the signals.
Analyze, modify and synthesizations of the signals.
In condition monitoring, signal processing means running a ANN, Fuzzy Logic or AI tools etc. to analyze the condition of the machine.

## Slide 31: Develop the practice of thinking positively because our minds are typically more predisposed to thinking negatively!
Figure 8: Simple digital signal processing bock diagram.

## Slide 32: As learners, we must put more of an emphasis on LISTENING than on working alone!
References:

## Slide 33: As learners, we must put more of an emphasis on LISTENING than on working alone!
References:
[4] OZTEMEL E. and GURSEV S., “Literature review of Industry 4.0 and related technologies,” J. Intell. Manuf., vol. 31, no. 1, pp. 127–182, 2020
[5] WAMBA S. F., AKTER S., EDWARDS A., CHOPIN G., and GNANZOU D., “How ‘Big Data’ can make big impact: Findings from a systematic review and a longitudinal case study,” Int. J. Prod. Econ., vol. 165, pp. 234–246, 2015
[6] KIM J. H., “A review of cyber-physical system research relevant to the emerging it trends: Industry 4.0, IoT, big data, and cloud computing,” J. Ind. Integration Manage., vol. 2, no. 3, 2017
[7] PACE F. De, MANURI F., and SANNA A., “Augmented reality in Industry 4.0,” Amer. J. Comput. Sci. Inf. Technol., vol. 6, no. 1, p. 17, 2018
[8] LU Y., “Cyber physical system (CPS)-based Industry 4.0: A survey,” J. Ind. Integration Manage., vol. 2, no. 3, 2017
[9] DILBEROGLU U. M., GHAREHPAPAGH B., YAMAN U., and DOLEN M., “The role of additive manufacturing in the era of Industry 4.0,” Procedia Manuf., vol. 11, pp. 545–554, 2017